## Slide 1
CHAPTER 1.
INTRODUCTION

## Slide 2: FIXED SPECTRUM ASSIGNMENT

## Slide 3: Fixed Spectrum Utilization
Maximum Amplitudes
Amplitude (dBm)
Heavy Use
Heavy Use
Medium Use
Sparse Use
Frequency (MHz)

## Slide 4: Fixed Spectrum Utilization
GHz
PSD (Power Spectrum Density)
Freq (GHz) | 0~1 | 1~2 | 2~3
Utilization(%) | 54.4 | 35.1 | 7.6
3~4 | 4~5 | 5~6
0.25 | 0.128 | 4.6
Measurements show that there is wide range of spectrum utilizations
across 6 GHz of spectrum

## Slide 5: Problems of Fixed Spectrum Utilization
Spectrum usage is concentrated on certain portions of the spectrum
A significant amount of the spectrum remains unutilized.
According to FCC (Federal Communication Commission):
Utilization of the fixed spectrum assignment is approx.
15-85% based on temporal and geographical variations
 Limited Available Spectrum and Inefficient Spectrum Usage!

## Slide 6: COGNITIVE RADIO NETWORKS; DYNAMIC SPECTRUM ALLOCATION NETWORKS (DSANs); xG INITIATIVE
Dynamic Spectrum
Allocation

## Slide 7: OVERALL VIEW
Dynamic Spectrum
Allocation
Applications
TCP/UDP
IP
MAC
Error Control
Physical
Adaptive
Protocol
Suite
Wireless LANs & MANs
Cellular
(2,3,4,5G)
Mesh Networks
Sensor
Networks
WiMAX

## Slide 8: COGNITIVE RADIO
A “Cognitive Radio” is the key enabling technology for Dynamic Spectrum Access!!
Capability to use or share the spectrum in an opportunistic manner.
“BANDWIDTH HARVESTING”
Dynamic spectrum access techniques allow the CR to operate in the
best available channel.

## Slide 9: SPECTRUM MANAGEMENT FRAMEWORK
1) Determine which portions of the spectrum is available and detect the
presence of licensed users when a user operates in a licensed band
(Spectrum Sensing)
2) Select the best available channel (Spectrum Decision)
3) Coordinate access to this channel with other users (Spectrum Sharing)
4) Vacate the channel when a licensed user is detected

## Slide 10: CRN COMMUNICATION FUNCTIONALITIES
Spectrum
Mobility
Function
Spectrum
Decision
Function
Sensing Information / Reconfiguration
Handoff Decision, Current and Candidate Spectrum Information
QoS Requirements
Reconfiguration
Routing Information/
Reconfiguration
Routing Information
Handoff Delay, Loss
Scheduling
Information/
Reconfiguration
Sensing
Information
Application Control
Link Layer
Delay
Link Layer
Transport
Network Layer
Physical Layer
Application
Spectrum
Sensing
Spectrum
Sharing

## Slide 11: BUILDING BLOCK: SOFTWATE DEFINED RADIO
SDRs: perform the majority of signal processing in the digital domain using programmable DSPs and hardware support
  Some signal processing is still done in the analog domain, such as in the RF and IF circuits
Get the software close to the antenna
Software defines the waveforms
Replace analog signal processing with digital signal processing
Some of the slides are from presentations by Eric Bloom and John Ackermann. Thank you.

## Slide 12: WHY SDR?
Flexible
Reduced Obsolescence
Enhances Experimentation
Brings Analog and Digital World Together
Quicker time to market
Multiple personalities (chameleon)
New things are possible:
  Multiple channels at the same time
  Better spectrum utilization
  “Cognitive Radios”

## Slide 13: New Breed of Radio
Reprogrammable
Multiband/Multimode
Networkable
Simultaneous voice, data, video
Full convergence of digital networks and radio science

## Slide 14: Disadvantages
Higher power consumption than dedicated ASIC approach
More MIPS required
Higher cost (today), but potential for lower cost in the future
Multi-band operation limited by antennas

## Slide 15: SOFTWARE ARCHITECTURE: GNU RADIO
GNU Radio: a library of signal processing blocks & the glue to tie it all together
The programmer builds a radio by creating a graph (as in graph theory)
  Vertices: signal processing blocks
  Edges represent the data flow between them
The signal processing blocks are implemented in C++
  Conceptually, blocks process infinite streams of data flowing (input ports to output ports)
  Blocks' attributes: the number of input and output ports as well as the type of data
  The most frequently used types are short, float and complex
Some blocks have only output ports or input ports (as data sources and sinks)
  There are sources that read from a file or ADC, and sinks that write to a file, DAC or graphical display
  About 100 blocks come with GNU Radio
  Writing new blocks is not very difficult

## Slide 16: Dial tone generator
Dial Tone Output
#!/usr/bin/env python
from gnuradio import gr
from gnuradio import audio
def build_graph ():
sampling_freq = 48000
ampl = 0.1
fg = gr.flow_graph ()
src0 = gr.sig_source_f (sampling_freq, gr.GR_SIN_WAVE, 350, ampl)
src1 = gr.sig_source_f (sampling_freq, gr.GR_SIN_WAVE, 440, ampl)
dst = audio.sink (sampling_freq)
fg.connect ((src0, 0), (dst, 0))
fg.connect ((src1, 0), (dst, 1))
return fg
if __name__ == '__main__':
fg = build_graph ()
fg.start ()
raw_input ('Press Enter to quit: ')
fg.stop ()
src0
src1
dst

## Slide 17: GNU Radio now has a nice GUI

## Slide 18: UNIVERSAL SOFTWARE RADIO PERIPHERAL
USB 2.0 interface
4 High-Speed AD Converters (64 MS/s, 12-bit Analog Devices AD9862)
4 High-Speed DA Converters (128 MS/s, 14-bit) to generate signals up to about 50 MHz (same chip as above)
Altera EP1C12 Q240C8 "Cyclone" FPGA for high bandwidth math, and to reduce the data rates to something you can squirt over USB2
Lots of digital, serial, and low speed analog IO for controlling daughterboards
2 Daughterboard slots to hold any RF receiver interface or tuner
2 Daughterboard slots to hold any RF transmitter

## Slide 19: Universal Software Radio Peripheral (USRP)

## Slide 20: GNU Radio resources
Home page (links to source code)
  http://www.gnu.org/software/gnuradio
Mailing list
  discuss-gnuradio-request@gnu.org
Archive
  http://mail.gnu.org/mailman/listinfo/discuss-gnuradio
Open source hardware
  http://www.opencores.org/projects/pci
  PCI bridges, ethernet, memory controllers, etc.