## Slide 1
CHAPTER 3. Architecture

## Slide 2: Cognitive Radio Network Architecture
Primary
Base Station
Primary
User
Primary Network
Licensed Band I
Unlicensed Band
Licensed Band II
CR Network
Access
Primary
Network
Access
CR User
Spectrum Band
CR
Base Station
Cognitive Radio Network
(With Infrastructure)
Other Cognitive Radio Networks
Spectrum Broker

## Slide 3: CR Ad Hoc Networks Architecture
Primary
Base Station
Primary
User
Primary Network
Licensed Band I
Unlicensed Band
Licensed Band II
Cognitive Radio Network
(Without Infrastructure)
CR
Ad Hoc
Access
CR User
Spectrum Band

## Slide 4: Cognitive Radio Network Architecture
Primary
Base Station
Primary
User
Primary Network
Licensed Band I
CR Network
Access
Primary
Network
Access
Cognitive Radio Network
(Without Infrastructure)
CR
Ad Hoc
Access
CR User
Spectrum Band
CR
Base Station
Cognitive Radio Network
(With Infrastructure)
Other Cognitive Radio Networks
Spectrum Broker
Unlicensed Band
Licensed Band II

## Slide 5: Architecture
Primary Network
(Primary User, Primary Base Station)
Cognitive Radio Network
(CR User, CR Base Station)
Spectrum Broker

## Slide 6: Primary Network
  An existing network infrastructure (or ad hoc network) which has an access right to a certain spectrum band.
  Example:
  Common cellular and TV broadcast networks.

## Slide 7: Primary User (or Licensed User)
Has a license to operate in a certain spectrum band.
This access can only be controlled by the primary base station and should not be affected by the operations of any other unlicensed users.
REMARK:
  PUs do not need any modification or additional functions for co-existence with CR base-stations and CR users.

## Slide 8: Primary Base Station (or Licensed Base-Station)
A fixed infrastructure network component which has a spectrum license such as BTS in a cellular system.
Does not have any CR capability for sharing spectrum with CR users.
It may be requested to have both legacy and CR protocols for the primary network access of CR.

## Slide 9: Cognitive Radio Network (or Dynamic Spectrum Access Network, or Secondary Network or Unlicensed Network)
Does not have license to operate in a desired band.
Hence, the spectrum access is allowed only in an opportunistic manner.
CR networks can be deployed both as an infrastructure network and an ad hoc network

## Slide 10: Cognitive Radio User (or Unlicensed User, Secondary User)
 has no spectrum license
  Hence, additional functionalities are required to share the licensed spectrum band.

## Slide 11: Cognitive Radio Base-Station (or Unlicensed Base Station or Secondary Base Station)
A fixed infrastructure component with CR capabilities.
CR base-station provides single hop connection to CR users without spectrum access license.
Through this connection, a CR user can access other networks.

## Slide 12: Spectrum Broker (or Scheduling Server)
A central network entity that plays a role in sharing the spectrum resources among different CR networks.
It can be connected to each network and can serve as a spectrum information manager to enable co-existence of multiple CR networks.

## Slide 13: Architecture
CR Network Access:
  CR users can access their own CR base-station both on licensed and unlicensed spectrum bands.
CR Ad Hoc Access:
  CR users can communicate with other CR users through ad hoc connection on both licensed and unlicensed spectrum bands.
Primary Network Access:
  CR users can also access the primary base-station through the licensed band.

## Slide 14: Classifications
CR Network on Licensed Band
  CR user is capable of using bands assigned to licensed users, apart from unlicensed bands, such as ISM band.
CR Network on Unlicensed Band
  CR can only utilize unlicensed parts of radio frequency spectrum.

## Slide 15: Cognitive Radio Network on Licensed Band
Primary User
Primary Base Station
Primary Network
CR User
CR Base Station
Cognitive Radio Network
Dynamic
Spectrum Access
CR User

## Slide 16: Cognitive Radio Network on Licensed Band
Temporally unused spectrum holes exist in the licensed spectrum band.
CR networks can exploit these spectrum holes through cognitive communication techniques.
In Figure, CR network coexists with the primary network at the same location and on the same spectrum band

## Slide 17: Cognitive Radio Network on Licensed Band
Main purpose of the CR network is to determine
the best available spectrum
Here in the licensed band, CR functions are aimed
at the detection of the presence of PUs
Channel capacity of the spectrum holes depends on the
interference at the nearby PUs

## Slide 18: Cognitive Radio Network on Licensed Band
Interference avoidance with PUs is the most important issue here
Also if PUs appear in the spectrum band occupied by CR users,
they should vacate the current spectrum band and move to
the new available spectrum immediately  spectrum handoff.

## Slide 19: Cognitive Radio Network on Unlicensed Band
Spectrum Broker
CR User
Cognitive Radio Network A
CR Base-Station
Cognitive Radio Network B
CR Base-Station
CR Ad Hoc Network

## Slide 20: CR Network on Unlicensed Band
Since there are no license holders, all network entities have the same right to access the spectrum bands.
Multiple CR networks co-exist in the same area and communicate using the same portion of the spectrum.
Intelligent spectrum sharing algorithms can improve the efficiency of spectrum usage and support high QoS.

## Slide 21: CR Network on Unlicensed Band
CR users focus on detecting the transmissions of other CR users.
Since all CR users have the same right to access the spectrum, CR users should compete with each other for the same unlicensed band.

## Slide 22: CR Network on Unlicensed Band
REQUIREMENTS:
Sophisticated spectrum sharing methods among CR users
Fair spectrum sharing among networks if multiple CR network operators reside in the same unlicensed band.