## Slide 1
CHAPTER 4.
COGNITIVE CYCLE

## Slide 2: Cognitive Cycle
  A CR determines appropriate communication parameters and adapts to the dynamic radio environment
  Tasks required for adaptive operation in open spectrum referred as COGNITIVE CYCLE.

## Slide 3: Spectrum Sensing
Spectrum
Sharing
Spectrum
Sensing
Spectrum
Decision
Channel Capacity
Primary User Detection
RF
Stimuli
Spectrum Hole
Radio Environment
Spectrum
Mobility
Decision Request
Transmitted Signal
Spectrum
Characterization

## Slide 4: Spectrum Sensing
  A CR monitors the available spectrum bands, captures
  their information, and then detects the spectrum holes.

## Slide 5: Spectrum Decision
Based on the spectrum availability, CR users can determine a channel.
This operation not only depends on spectrum availability, but it is also determined based on internal (and possibly external) policies.

## Slide 6: Spectrum Sharing
Multiple CR users try to access the spectrum
CR network access should be coordinated in order to prevent multiple users colliding in overlapping portions of the spectrum.

## Slide 7: Spectrum Mobility
CR users are regarded as "visitors" to the spectrum.
If PUs need a specific portion of the spectrum then the CR users must continue in another vacant portion of the spectrum.

## Slide 8: Reconfigurability
Capability of adjusting operating parameters for the transmission on-the-fly without any modifications on the hardware components.
This capability enables CR to adapt easily to the dynamic radio environment.

## Slide 9: Reconfigurable Parameters
  Operating Frequency
  Modulation
  Transmission Power
  Communication Technology

## Slide 10: Operating Frequency
A CR is capable of changing the operating frequency.
Based on the information about the radio environment, the most suitable operating frequency can be determined and
the communication can be dynamically performed on this appropriate operating frequency.

## Slide 11: Modulation
A CR should reconfigure the modulation scheme adaptive to the user requirements and channel conditions.
Example: Delay Sensitive Applications  data rate important
 Modulation scheme enabling higher spectral efficiency!!
Example: Loss-Sensitive Applications  error rate important !
 Modulation scheme with low bit error rate..

## Slide 12: Transmission Power
Transmission power can be reconfigured within the power constraints.
If higher power operation is not necessary, CR reduces the transmitter power to a lower level to allow more users to share the spectrum and to decrease the interference.

## Slide 13: Communication Technology
  A CR can be used to provide interoperability among different communication systems.

## Slide 14: Reconfigurable Parameters
Not only at the beginning of a transmission but also during the transmission.
Parameters can be reconfigured such that
  CR is switched to a different spectrum band
  Tx and Rx parameters are reconfigured
  Appropriate communication protocol parameters and modulation schemes are used.